## Slide 1
CS447 Recitation: 9/30/16 (Lab #4, Week 5)
Agenda for today:
General explanation of today’s lab (midterm review).
Pass around handout, sign-in sheet
Quick review of some specific concepts
  These slides and the lab are available online:
  https://github.com/kc13/CS447

## Slide 2
Procedure for today:
  The main objective today is to review specific aspects of the course material in advance of the midterm.
  There is a lab assignment:
    It will be distributed as hardcopy, since there are exercises to be done by hand.
    Be sure to put your name on the handout and turn it in, either when you get done (if you finish before recitation ends), or when recitation ends.
    Any reasonable attempt at some/all of the problems will be sufficient to receive full credit for today’s lab.
    There is no need to submit anything on Courseweb this week.

## Slide 3
Quick review of specific concepts
Binary  hexadecimal
AND operations, and their use to extract bitfields
Using branching to replicate an if statement with && or || in the condition

## Slide 4
Conversion between hexadecimal and binary
0xabcd1234
0xabcd1234
One method (see example on board):
For each digit from most significant to least:
- write down its corresponding decimal representation
For each decimal representation:
- convert to binary (expect 4 bits per original hex digit)
If you start with binary:
For each group of 4 bits:
- write down its corresponding decimal representation
For each decimal representation:
- convert to hex (expect 1 digit per 4 original bits)

## Slide 5
Bitwise and (&)
Assume x = 20 and y = 15
What is x & y?
One method (see example on board):
For each decimal value:
convert to binary
Line up the two representations, with one above the other.
Perform the and test on each bit.
In binary, it can be helpful to think of bitwise and in many ways:
As vector multiplication
As one bitstring being applied as a “mask” of the other (see next slide)

## Slide 6
Bitwise and (&) as a mask for a bitfield
R-type instruction format, MIPS Green Sheet
R-type instruction format, another view:
How can we get the $funct value in isolation, in register $t1?
Assume the 32 bit value representing this instruction is in $t0.
As a mask, the bitstring 00111111 (with all leading digits set to 0) could be applied as a mask to $t0.
This can be accomplished with andi, $t1, $t0, 63
equivalently: andi, $t1, $t0, 0x3f

## Slide 7
Using branching to replicate an if statement with && or || in the condition
if (t1 == 10 || t2 > 20) {
System.out.println(“message 1”)
}
else {
System.out.println(“message 2”)
}
Do more things…

## Slide 8
if (t1 == 10 && t2 > 20) {
System.out.println(“message 1”)
}
else {
System.out.println(“message 2”)
}
Do more things…
bne $t1, 10, elseBlock
blt $t2, 21, elseBlock
elseBlock:
syscall for printing message 2
thenBlock:
syscall for printing message 1
resume:
instructions to do more things
j resume